## Slide 1: Proving Safety in Aircraft Systems
J Tanner Slagel
NASA Langley Research Center
Henson Seminar Series
Salisbury University
Oct 4th, 2023

## Slide 2
F-16 Close Call 5/5/16
[1]: Source, NASA Armstrong: https://www.youtube.com/watch?v=aSzXqlnT7nQ&embeds_euri=https%3A%2F%2Fwww.nasa.gov%2F&source_ve_path=MjM4NTE&feature=emb_title
Notes: Hey Everyone welcome, let's start by watching a video This video is of a F-16 in 2016 almost crashing just a spoiler alert it doesn't crash and the pilot ends up being fine:
Alright so what did we just see. This video is of the HUD display of a student pilot from the Arizona Air National Guard’s 152nd Fighter Squadron, and the pilot executes a maneuver and because of the resulting 8.2 G forces the Pilot loses consciousness
About 11 seconds later the F-16 is pointed 50 degree below the horizon, going a little over the speed of sound at 11.8 thousand feet. In this situation the 'floor' is 12,000 feet which is considered the minimal acceptable altitude for the F-16 to be at.
Four seconds later the aircraft is at 8570 feet, so lost about 3500 feet in 4 seconds, and the AUTO-GCAS system activates, performing a 'Fly UP' maneuver at where it takes control of the F-16 while the pilot is incapacitated. The maneuver results in a force of 9.1 Gs, but it pulls the noise of the F-16 up and eventually the pilot recovers and the F-16 gets back above the 'floor' of 12,000 ft.
So Auto-Gcas eps the the automatic ground collision avoidance system that has been developed over several decades for situations like these, developed by Lockheed Martin and NASA Armstrong and the Airfare research laboratory not by my be at all). And what we just saw is an example of this technology saving a pilot's life.

## Slide 3
18
Play-by-play
30
33
38
41
65
8.2 G Maneuver
Pilot loses
consciousness
F-16 Close Call 5/5/16

## Slide 4
F-16 Close Call 5/5/16
18
Play-by-play
30
33
38
41
65
Pilot loses
consciousness
Drops below ‘floor’
8.2 G Maneuver

## Slide 5
F-16 Close Call 5/5/16
18
Play-by-play
30
33
38
41
65
Pilot loses
consciousness
Drops below ‘floor’
55º below horizon
Auto-GCAS
Activates
8.2 G Maneuver
[2]: Auto GCAS, Lockheed Martin: https://www.lockheedmartin.com/en-us/products/autogcas.html

## Slide 6
F-16 Close Call 5/5/16
18
Play-by-play
30
33
38
41
65
Pilot loses
consciousness
Drops below ‘floor’
55º below horizon
Auto-GCAS
Activates
9 G maneuver
8.2 G Maneuver

## Slide 7
F-16 Close Call 5/5/16
18
Play-by-play
29
33
38
41
65
Pilot loses
consciousness
Drops below ‘floor’
55º below horizon
Auto-GCAS
Activates
9 G maneuver
Back above ‘floor’
8.2 G Maneuver

## Slide 8
[2]: Runtime Assurance Framework Development For Highly Adaptive Flight Control Systems, SBIR Phase III Report, J.D. Schierman et. al. https://apps.dtic.mil/dtic/tr/fulltext/u2/1010277.pdf
Advanced System
Reversionary System
Trusted
Output
RTA Monitor &
Switch Mechanism
System
Being
Controlled
Output
Untrusted
Trusted
Output
Input
Allocator
Runtime Assurance (RTA)

## Slide 9
[3]: Run-Time Assurance: A Rising Technology, J. G. Fuller, 2020 DASC https://ieeexplore.ieee.org/document/9256425
Human Pilot
Auto-GCAS
Trusted
RTA Monitor &
Switch Mechanism
Flying an
F-16
Input
Allocator
Output
Untrusted
Trusted
Output
Output
Auto-GCAS

## Slide 10
[3]: Run-Time Assurance: A Rising Technology, J. G. Fuller, 2020 DASC https://ieeexplore.ieee.org/document/9256425
But wait!
How do we know
  Auto-GCAS works?
  RTA works?
  F-16s work?

## Slide 11
Software
  Aircraft (ex. detect and avoid)
  Cybersecurity
  Medical Equipment
  Neural Networks, large language models
Hardware
  Computer processors
  Fingerprint readers
  Avionics
Systems
  National airspace/ urban airspace
  Autonomous vehicles
  Aircraft, Spacecraft
  Power plants
  Missile defense systems
[4]: Why Is Formal Methods Necessary? LaRC FM Webpage: https://shemesh.larc.nasa.gov/fm/fm-why-new.html
Safety- and Mission-critical Operations
Catastrophic failures can happen!
Decade of development - $7 billion
Cargo – $500 million
Overflow error
Explosion of Ariane 5 rocket, 1996

## Slide 12
Software
  Aircraft (ex. detect and avoid)
  Cybersecurity
  Medical Equipment
  Neural Networks, large language models
Hardware
  Computer processors
  Fingerprint readers
  Avionics
Systems
  National airspace/ urban airspace
  Autonomous vehicles
  Aircraft, Spacecraft
  Power plants
  Missile defense systems
Safety- and Mission-critical Operations
Catastrophic failures can happen!
Missile defense system, failed to intercept missile
28 dead, 100 injured
Accumulation of Floating point error from constant execution
Patriot Missile Failure, 1991
[4]: Why Is Formal Methods Necessary? LaRC FM Webpage: https://shemesh.larc.nasa.gov/fm/fm-why-new.html

## Slide 13
Software
  Aircraft (ex. detect and avoid)
  Cybersecurity
  Medical Equipment
  Neural Networks, large language models
Hardware
  Computer processors
  Fingerprint readers
  Avionics
Systems
  National airspace/ urban airspace
  Autonomous vehicles
  Aircraft, Spacecraft
  Power plants
  Missile defense systems
Safety- and Mission-critical Operations
Catastrophic failures can happen!
Defective Hardware Recall - $475 million
Division inaccurate beyond 3 digits
Pentium FDIV bug, 1996
[4]: Why Is Formal Methods Necessary? LaRC FM Webpage: https://shemesh.larc.nasa.gov/fm/fm-why-new.html

## Slide 14
Software
  Aircraft (ex. detect and avoid)
  Cybersecurity
  Medical Equipment
  Neural Networks, large language models
Hardware
  Computer processors
  Fingerprint readers
  Avionics
Systems
  National airspace/ urban airspace
  Autonomous vehicles
  Aircraft, Spacecraft
  Power plants
  Missile defense systems
[5]: Apache Log4j Vulnerability Guidance, CISA, https://www.cisa.gov/news-events/news/apache-log4j-vulnerability-guidance
Safety- and Mission-critical Operations
Catastrophic failures can happen!
Loging software for Amazon Cloud Services,
Apple iCloud, Minecraft
User can log arbitrary code to run on target computer or server
Log4j Vulnerability, 2022

## Slide 15
Safety- and Mission-critical Operations
Actual distance 194.89 miles
Wrong!
Chat GPT:
How can we assure critical software and hardware?

## Slide 16
[6]: What is Formal Methods? LaRC FM Webpage https://shemesh.larc.nasa.gov/fm/fm-what.html
What is Formal Methods?
‘Applying mathematically rigorous techniques for specification and verification of software and/or hardware’
  Formal specifications are well-formed statements in a mathematical logic
  Formal verification uses a set of inference rules to prove properties of formal specifications
Experimentation is not enough in safety-critical applications

## Slide 17
What is Formal Methods?
Let’s do some Formal Methods!!
[6]: What is Formal Methods? LaRC FM Webpage https://shemesh.larc.nasa.gov/fm/fm-what.html

## Slide 18
Wildfire fighting operations require situational awareness
Unmanned aircraft system pilot kit (UASP-kit)
Operational volumes (OV)
  Mission area
  Alerting volume
Alerting system
[7]: NASA System-Wide Safety Wildland Firefighting Operations Workshop Report, S. Lehman Et Al., Tech Report 2022, https://ntrs.nasa.gov/citations/20220014721 [8]: Developing an Unmanned Aircraft System Pilot Kit (UASP-kit) for Wildland Fire UAS Operators, L. Martin Et Al., AIAA AVIATION 2022

## Slide 19
Wildfire fighting operations require situational awareness
Unmanned aircraft system pilot kit (UASP-kit)
Operational volumes (OV)
  Mission area
  Alerting volume
Alerting system
[7]: NASA System-Wide Safety Wildland Firefighting Operations Workshop Report, S. Lehman Et Al., Tech Report 2022, https://ntrs.nasa.gov/citations/20220014721 [8]: Developing an Unmanned Aircraft System Pilot Kit (UASP-kit) for Wildland Fire UAS Operators, L. Martin Et Al., AIAA AVIATION 2022

## Slide 20
Wildfire fighting operations require situational awareness
Unmanned aircraft system pilot kit (UASP-kit)
Operational volumes (OV)
  Mission area
  Alerting volume
Alerting system
[7]: NASA System-Wide Safety Wildland Firefighting Operations Workshop Report, S. Lehman Et Al., Tech Report 2022, https://ntrs.nasa.gov/citations/20220014721 [8]: Developing an Unmanned Aircraft System Pilot Kit (UASP-kit) for Wildland Fire UAS Operators, L. Martin Et Al., AIAA AVIATION 2022

## Slide 21
Wildfire fighting operations require situational awareness
Unmanned aircraft system pilot kit (UASP-kit)
Operational volumes (OV)
  Mission area
  Alerting volume
Alerting system
[7]: NASA System-Wide Safety Wildland Firefighting Operations Workshop Report, S. Lehman Et Al., Tech Report 2022, https://ntrs.nasa.gov/citations/20220014721 [8]: Developing an Unmanned Aircraft System Pilot Kit (UASP-kit) for Wildland Fire UAS Operators, L. Martin Et Al., AIAA AVIATION 2022

## Slide 22
Wildfire fighting operations require situational awareness
Unmanned aircraft system pilot kit (UASP-kit)
Operational volumes (OV)
  Mission area
  Alerting volume
Alerting system
[7]: NASA System-Wide Safety Wildland Firefighting Operations Workshop Report, S. Lehman Et Al., Tech Report 2022, https://ntrs.nasa.gov/citations/20220014721 [8]: Developing an Unmanned Aircraft System Pilot Kit (UASP-kit) for Wildland Fire UAS Operators, L. Martin Et Al., AIAA AVIATION 2022

## Slide 23
Scenario: comparing alerting volumes
“The OV is not contained in the red
alerting volume.”
but
“The sUAS is within to the OV, but there is not a ‘red’ alert.”
[8]: Scenario based on Figure 7 in: Developing an Unmanned Aircraft System Pilot Kit (UASP-kit) for Wildland Fire UAS Operators, L. Martin Et Al., AIAA AVIATION 2022

## Slide 24
“The OV is contained in the red
alerting volume.”
“The sUAS is within to the OV and there is a ‘red’ alert.”
Scenario: comparing alerting volumes
[8]: Scenario based on Figure 7 in: Developing an Unmanned Aircraft System Pilot Kit (UASP-kit) for Wildland Fire UAS Operators, L. Martin Et Al., AIAA AVIATION 2022

## Slide 25
“The OV is contained in the red
alerting volume.”
“The sUAS is within to the OV and there is a ‘red’ alert.”
[8]: Scenario based on Figure 7 in: Developing an Unmanned Aircraft System Pilot Kit (UASP-kit) for Wildland Fire UAS Operators, L. Martin Et Al., AIAA AVIATION 2022
Scenario: comparing alerting volumes

## Slide 26
Operational volumes (OVs)
OVs as datatype in PVS
Algorithms
  Point-in
  Intersection & containment
Example: Let
then
“The conforming alerting volume contains the polygon.”
Result: formal verification of OVs
[9]: Formalized Reasoning of Operational Volumes for Wildland Fire Fighting, J Tanner Slagel Et Al., AIAA AVIATION 2023

## Slide 27
Example: Let
then
“If a point has a distance to the polygon of at most , then that point is in the alerting volume ”
Operational volumes (OVs)
OVs as datatype in PVS
Algorithms
  Point-in
  Intersection & containment
Result: formal verification of OVs
[9]: Formalized Reasoning of Operational Volumes for Wildland Fire Fighting, J Tanner Slagel Et Al., AIAA AVIATION 2023

## Slide 28
Formal Methods

## Slide 29
Advanced System
Reversionary System
Geofenced Operations

## Slide 30
Complex Path
Trusted
Output
RTA Monitor &
Switch Mechanism
Operating a
fix-winged
aircraft
Return to safe zone dynamics
Input
Allocator
Geofenced Operations
Output
Untrusted

## Slide 31: How do we model and analyze these systems at design time?
Complex Path
Trusted
Output
RTA Monitor &
Switch Mechanism
Return to safe zone dynamics
Input
Allocator
Geofenced Operations
Operating a
fix-winged
aircraft
Output
Untrusted

## Slide 32: Hybrid Programs and Differential Dynamic Logic

## Slide 33: Hybrid Programs
Hybrid programs allow formal specification of hybrid systems:
  Discrete jump set:
  Differential equations:
    variables
    assignments (e.g. – functions of existing variable values)
    first order formula that describes domain
Example:

## Slide 34: Hybrid Programs
Example:

## Slide 35: Hybrid Programs (continued)
For hybrid programs , , first-order formula :
  Choice
  Sequence
  Repeat
  Test
Example:
*

## Slide 36: Hybrid Programs (continued)
Example:
*

## Slide 37: Hybrid Programs (continued)
Example:
*

## Slide 38: Hybrid Programs (continued)
Example:
*
This is a Dubins path!

## Slide 39: : Differential Dynamic Logic
allows formal reasoning of hybrid programs:
For hybrid program and predicate
  All runs P
  Some runs P
Example: Let
,
then

## Slide 40: : Differential Dynamic Logic
Example: Let
,
then

## Slide 41: : Differential Dynamic Logic – Rule Schema
Union axiom:
Loop rule:
Differential invariant
rule:
….and many more
[10] Differential Dynamic Logic, Logical Foundations of Cyber-Physical Systems. André Platzer. 2018 https://doi.org/10.1007/978-3-319-63588-0
[11] “Cheat Sheet,” André Platzer, https://symbolaris.com/logic/dL-sheet.pdf

## Slide 42: : Proof
Differential invariant
rule:
[10] Differential Dynamic Logic, Logical Foundations of Cyber-Physical Systems. André Platzer. 2018 https://doi.org/10.1007/978-3-319-63588-0
[11] “Cheat Sheet,” André Platzer, https://symbolaris.com/logic/dL-sheet.pdf

## Slide 43: : Proof
Differential invariant
rule:
[10] Differential Dynamic Logic, Logical Foundations of Cyber-Physical Systems. André Platzer. 2018 https://doi.org/10.1007/978-3-319-63588-0
[11] “Cheat Sheet,” André Platzer, https://symbolaris.com/logic/dL-sheet.pdf

## Slide 44: : Proof
Differential invariant
rule:
Apply Di rule
[10] Differential Dynamic Logic, Logical Foundations of Cyber-Physical Systems. André Platzer. 2018 https://doi.org/10.1007/978-3-319-63588-0
[11] “Cheat Sheet,” André Platzer, https://symbolaris.com/logic/dL-sheet.pdf

## Slide 45: : Proof
Differential invariant
rule:
Apply Di rule
Apply
substitution
[10] Differential Dynamic Logic, Logical Foundations of Cyber-Physical Systems. André Platzer. 2018 https://doi.org/10.1007/978-3-319-63588-0
[11] “Cheat Sheet,” André Platzer, https://symbolaris.com/logic/dL-sheet.pdf

## Slide 46: : Proof
Differential invariant
rule:
Apply Di rule
Apply
substitution
Arithmetic!
[10] Differential Dynamic Logic, Logical Foundations of Cyber-Physical Systems. André Platzer. 2018 https://doi.org/10.1007/978-3-319-63588-0
[11] “Cheat Sheet,” André Platzer, https://symbolaris.com/logic/dL-sheet.pdf

## Slide 47: dL
Plaidypvs
[12] Towards an Implementation of Differential Dynamic Logic in PVS, SOAP 2022, Slagel et. al. https://dl.acm.org/doi/abs/10.1145/3520313.3534661
Notes: Properly Assured Implementation of Differential Dynamic Logic from hybrid programs verification and specification

## Slide 48: RTA in Plaidypvs
Example: Define
While S is true run with monitor
While S is not true run
and

## Slide 49
RTA in Plaidypvs
“If is safe in S and is always safe, then the RTA architecture is always safe”
Example:

## Slide 50
Advanced System
Reversionary System
Geofenced Operations (simplified)

## Slide 51: Geofence RTA
and
“The aircraft never goes into the red region ”
“If the aircraft exits the blue region, it will
Eventually return to the blue region ”

## Slide 52
Conclusion
[6]: What is Formal Methods? LaRC FM Webpage https://shemesh.larc.nasa.gov/fm/fm-what.html
Formal Methods can be used to assure safety- and mission-critical systesms
Questions, comments?
Thank you for paying attention!
J.Tanner.Slagel@nasa.gov